## Slide 1: VTS access arrangement revisions Cost allocation methodology and tariffs
Alex Curran

## Slide 2: Overview
AER draft decision approved SWP expansion capex
APA proposed cost recovery arrangements for SWP expansion capex
AER draft decision approach to cost recovery
Implementation issues
APA revised proposal for SWP expansion capex cost recovery
Summary of outcomes from proposed approach

## Slide 3: AER DD approved VTS investment to increase SWP capacity
Project | Capacity | Cost | Timing
Current | E: 412TJ/day; W: 104TJ/day | - | -
BCS reconfiguration and Winchelsea bidirectionality | E: 412TJ/day; W: 147TJ/day | $3.5m | March 2018
WORM project | E: 435TJ/day; W: 220TJ/day | $122.4m | end 2020
Drivers for investment
Insufficient capacity to support Iona refill at current capacity
  Existing ‘tightness’ and system security concerns from insufficient storage volumes for winter 2018
  Increased operation of Laverton Nth GPG reduces opportunities for refill
Operational benefits
  Linepack balancing, GPG readiness, gas on gas competition, lower fuel gas costs
Reduced reliance on Brooklyn compressor station site
  Brooklyn is a congested site and expansion options are limited
Iona storage expansion plans – Advice to AEMO
  2017 - reservoir withdrawal from 390TJ/day to 440TJ/day; injection capacity from 153TJ/day to 173TJ/day
  End 2019 - reservoir withdrawal from 440TJ/day to 570TJ/day; injection capacity from 173TJ/day to 250 TJ/day

## Slide 4: APA proposed cost recovery arrangements for augmentation projects
Current Iona refill tariff
  Currently ‘Nominal’ tariff of $0.0539/GJ
  Does not reflect asset costs as flows assumed to be ‘off-peak’ and not driving congestion/investment
  Flows from Longford, Pakenham and Culcairn pay only Iona refill tariff
    No refills expected on a peak injection day so no injection tariff payable
BCS reconfiguration and Winchelsea bidirectionality
  Additional expenditure for BCS reconfiguration and Winchelsea bidirectionality project allocated directly to Iona refill tariff
    Partial move away from ‘nominal’ approach to reflect that Iona refill was now driving investment (no longer only offpeak)
  Iona refill tariff proposed at $0.079/GJ; equals $0.025/GJ uplift to base tariff
Western Outer Ring Main
  Situated in Metro South East tariff zone
  WORM expenditure included in tariff model and allocated using same methodology as other capex
    Allocated to relevant flow paths in proportion to volume
    Primary contributors to WORM costs are users of Metro zones, Cross system tariff, Calder

## Slide 5: AER DD cost recovery arrangements for augmentation projects
AER approved as filed:
  Direct allocation of BCS reconfiguration and Winchelsea bidirectionality project costs to Iona refill tariff
  Inclusion of WORM costs as per APA VTS broader cost allocation methodology
AER required revision:
  Application of the cross system tariff to Iona system withdrawal refill volumes that are subsequently directed to South Australia (using the SEA Gas Pipeline)
  Intended result would be for injections from Culcairn, Longford, and Pakenham, that went to SA via the Iona facility, the 2018 tariff charged (as per AER DD) would be:
    Iona refill ($0.079/GJ) + Cross system tariff-D ($0.1614/GJ)
AER stated drivers for draft decision (AER 2017: page 10-19):
  Some users of the VTS may not be contributing their share towards the cost of the VTS
  Victorian gas customers may end up subsidizing South Australian customers

## Slide 6: Derivation of cross system tariff
Cross system tariff
  Applies to flows that ‘cross the system’
    Conceptually, tariff applies to withdrawals that are matched to an injection point that is not the closest to the withdrawal
  Tariff is equivalent to the Metro zone tariffs minus an allocation of common costs
    Common costs include non-system assets, corporate and admin. costs, EBSS carry overs, debt raising costs
    Relates to direct costs of using system assets as per physical flow path
  Cross system tariff volumes are not forecast, and all revenue is returned to users through the tariff variation mechanism by reducing the target revenue in later years of the period
    APA receives no benefit from cross system flow volumes (higher or lower)

## Slide 7: Difficulties implementing AER draft decision to apply cross system tariff to Iona volumes destined for South Australia
APA VTS does not have access to metering data – relevant pipes not part of APA VTS system
  APA VTS has no meaningful way of identifying Longford – Iona UGS – South Australia flows for billing purposes
  Iona UGS connection to SEA Gas Pipeline is in Iona compound and not owned/accessed by APA VTS
‘Temporal’ limitations to identifying relevant gas flows
  Gas that travels across the VTS and into Iona UGS may stay in storage for some time before being either reinjected into Victoria or sent to SA
  Could not know whether gas should be subject to cross system tariff until leaves storage which may be long after billing
  Monthly billing would not be able to track and effectively allocate the cross system tariff to these volumes
Identification of ‘Longford’ rather than ‘Port Campbell’ gas as flowing to SA
  The Iona facility is filled (primarily) via gas from Port Campbell and Longford
  Gas comingled in storage, which may be directed to Victoria or South Australia
  Not possible to identify whether gas flowing to South Australia was from Longford to allocate tariff

## Slide 8: APA revised proposal in response to AER DD
APA VTS noted drivers for the AER draft decision
  Ensuring user pays approach – allocation of costs to those that drive them
  Limiting cross subsidies between users
In implementing the AER’s draft decision, APA VTS concluded that these policy drivers supported application of the cross system tariff to all ‘cross system’ Iona withdrawal point volumes
APA VTS proposed removing the exclusion on section A.3(d) of the access arrangement
  Applies cross system tariff to all ‘cross system’ Iona withdrawal point volumes
  Aligns tariff treatment of Iona UGS withdrawals with SEA Gas withdrawals (they are in close proximity)
  Limits current incentives to preferentially use Iona UGS withdrawal point instead of SEA Gas withdrawal point for SA flows due to differing cross system tariff treatment

## Slide 9: Summary outcomes
Iona refill from Longford (and other injection points) use the VTS and have driven capital expenditure
  Iona refill no longer an ‘off-peak’ activity that does not drive costs so case for discounted tariff no longer relevant
Supply from Iona storage one of a number of supply options in peak
  Creates degree of equivalence between options by ensuring use of system is not subsidised by others
APA VTS earns no additional revenue from application of the cross system tariff to ‘cross system’ Iona withdrawal point volumes
  All cross system revenue is returned to customers through the tariff variation mechanism
Reduces withdrawal tariffs in later years of period as revenue returned
  Allocates full cross system charge to volumes that are sent to SA (not returned to VTS)
  Returns part of cross system charge in respect of volumes that are reinjected back into VTS
Equivalent treatment to other system withdrawal points
  Iona withdrawal point volumes treated the same as SEA Gas withdrawal volumes in the same compound